## Slide 1
Improvements to the Kigen Solver
Jordan Taylor 313D

## Slide 2: Overview
Introduction
Background
Research Questions
Methods and Experiments
Conclusions
Future Work

## Slide 3: About Me
Rising 3rd year at Georgia Tech
Studying Computer Science and Math
Research Interests:
Decision Theory
Reinforcement Learning
Optimization
Approximation Algorithms
Meta-Learning

## Slide 4: What is Kigen?
Design Space Exploration and Optimization Tool
Engineer defined trade space, objectives and constraints
Kigen
Set of Pareto Efficient Designs
Input
Output
Notes: 5

## Slide 5: The Kigen Modeling Language (KigenML)
Design Problem Definition in KigenML
/* Domain description */ type ConstellationMission { var spacecraft : Spacecraft [ 2 .. 50 ] fun cost = { …// Some complex function fun benefit = { … // Another function constraint atLeast2SC: filter( spacecraft, (s : Spacecraft) => s.payload != null ).size > 1) } type Spacecraft { var payload : Payload [ 0 .. 1 ] } abstract type Payload type InterferometryPayload extends Payload
/* Initial conditions */ model myMission of ConstellationMission { model sc1 of Spacecraft in spacecraft model sc2 of Spacecraft in spacecraft { model p1 of InterferometryPayload in payload } } /* Define optimization criteria */ minimize myMission.cost maximize myMission.benefit solve optimize using 'nsgaii' 30 times with populationSize 100, maxGenerations 20, maxSolutionLength 15
Able to derive domain model and reason about how to explore the space
Notes: Spend 2 minutes here
Think of a mathematical programming language
Extension to include structures
Mix of quadratic programming language, a bit of general purpose language, and flavors of model finders: e.g., MIT’s Alloy, and Microsoft FORMULA (TODO: Find a good definition for these)
model finding tools and satisfiability checkers

## Slide 6: Kigen Explained
Trade Space is
Represented
Designs are
Analyzed
User
Initial Model is
Created to
Search from
Transformation
Rules are Created
Trade Space
is Searched
Kigen
Compiled to
EMF
m : Mission
m : Mission
sc : S/C
Left hand side (Condition)
Right hand side (Operation)
NEW
NEW
sc
Rule “addSpacecraft”
Add Spacecraft
Add Comm Link
Add Spacecraft
Add X-Band Comm
Solution Representation
Add Spacecraft
Add Comm Link
Add Spacecraft
Add Ka-Band Comm
Add Spacecraft
Add X-Band Comm
Add Payload
Add Spacecraft
Add Ka-Band Comm
Crossover
Mutation

## Slide 7: Background
Motivating Case Study: Spacecraft-Based Radio Interferometry
Radio interferometers:
Radio telescopes consisting of multiple antennas
Achieve the same angular resolution as that of a single telescope with the same aperture
 Typically ground-based
Want to do this in space:
Frequencies < 30Mhz blocked by ionosphere
Cluster of spacecraft (3 – 50) functioning as telescopes in LLO
 CubeSats or SmallSats are promising enablers for this
Source: http://www.passmyexams.co.uk/GCSE/physics/images/radio-telescopes-outdoors.jpg
Notes: 17
that receive radio waves from the same astronomical object
Interesting to observe, e.g., galaxies
Narrowed down to cluster of spacecraft acting as antennas in lower lunar orbit; all small spacecraft under 100 kilogram
Transition: when first looking at the problem, seems fairly simple

## Slide 8: Background
Results from Multi-Spacecraft Interferometry Mission

## Slide 9: Background
Motivating Case Study: Multi-Rover Mars Cave Exploration
Why Explore Caves on Mars?
Possibility for human settlement
Understanding the planet’s evolution
Search for Extraterrestrial Life
Why use Multiple Rovers?
To Improve Fault Tolerance
To perform science deeper in the caves
Notes: 17
that receive radio waves from the same astronomical object
Interesting to observe, e.g., galaxies
Narrowed down to cluster of spacecraft acting as antennas in lower lunar orbit; all small spacecraft under 100 kilogram
Transition: when first looking at the problem, seems fairly simple

## Slide 10: Research Questions
Runtime
Quality
It can take a long time to find a feasible solution
Will starting the search from a small model that satisfies some requirements decrease the time needed to find a feasible solution?
Autonomously generated exploration rules underperform those created by domain experts, increasing the workload of users and the number of iterations needed to find quality solutions
Can autonomously generated rules perform comparably to those created by domain experts, making Kigen easier to use?
Almost all research in the field of model-based design has used a genetic algorithms to find solutions
Can other algorithms search the model-space better than a genetic algorithm?
Want to Improve

## Slide 11: Research Questions
Will starting the search from a small, feasible model decrease the time needed to find a solution?
Can autonomously generated rules outperform those created by domain experts?
Can other algorithms search the model-space better than a genetic algorithm?

## Slide 12: Improving Starting Location of Search
Methodology
Feasible Model
Space
Feasible Model Space: Set of Designs that Satisfy All Multiplicity Requirements
Example Requirement: A mission must have between 2 and 10 rovers
Mission
Rover
Rover
Mission
Rover
In Feasible Model
Space
Not in Feasible
Model Space
Feasibility Region: Set of Designs that Satisfy All Requirements
Feasibility
Region
Current Method
Start searching from an empty model unless otherwise specified by the user
Proposed Method
Start searching from the smallest feasible model using what is specified by the user

## Slide 13: Improving Starting Location of Search
Application to Case Study: Multi-Rover Mars Cave Exploration Mission
Subset of Requirements
A RoverConstellation must have between 2 and 10 Rovers
A RoverConstellation must have a BaseStation
A Rover must have a Camera and an EnvironmentSensor
RoverConstellation
Rover
Camera
Current Starting Model
(Without Any User Guidance)
RoverConstellation
EnvSensor
Rover
Camera
EnvSensor
Proposed Starting Model
(Without Any User Guidance)
BaseStation

## Slide 14: Improving Starting Location of Search
Experimental Results
On Average 5,770 Fewer Designs Evaluated to Find a Feasible Mars Cave
Exploration Design, Decreasing Time to Find a Feasible Solution by !

## Slide 15: Research Questions
Will starting the search from a small, feasible model decrease the time needed to find a solution?
Can autonomously generated rules outperform those created by domain experts?
Can other algorithms search the model-space better than a genetic algorithm?

## Slide 16: New Exploration Rules: Method
Mission
Rover
Rover
A Mission
contains
2 to 5 rovers
A Rover
contains 1 to 3
Instruments
addMissionRule
addRoverRule
Rover
Instrument
+
=
Mission
Rover
Instrument
Rover
Instrument
Current: Small Atomic Rules
Proposed: Rules Made by Combining Multiplicity Requirements
A Mission contains 2 to 5 rovers AND a Rover contains 1 to 3 Instruments

## Slide 17: New Exploration Rules: Results
Experiment Setup:
Ran a genetic algorithm 5 times with a solution length of 150, population size of 1000 and 100 generations using the current rules then the new rules
New rules did not increase solution quality
Current vs New Rule Comparison: Interferometry Mission Design
Solutions found using New Rules
Solutions found using Current Rules

## Slide 18: New Exploration Rules: Results
Why did the Current Rules Outperform the New Rules?
New Proposal: Use BOTH the current and more complex rules to better search the entire model space
Feasible Model Space
For an equal solution length, the current exploration
rules’ search space is limited to smaller models
For an equal solution length, the new exploration
rules’ search space is limited to larger models
0
# 3U
CubeSats
# 6U CubeSats
#
SmallSats

## Slide 19: New Exploration Rules: Results
Current vs New Rule Comparison on the Interferometry Mission
= Worse w.r.t Solutions Found in the Experiment Being Compared with
Solutions Found Using Current Rules
Solutions Found Using New Rules
(Both Simple and Complex)
Current Rules Better Searched Region Corresponding to Smaller Models because only a Small Portion of the Feasible Model Space is Reachable
New Rules Better Searched the Whole Design Space because more of the Feasible Model Space can be Reached

## Slide 20: New Exploration Rules: Results
Expert Crafted Rules vs New Rules on the Interferometry Mission
With all else equal, of the designs found by expert crafted rules, 63% were improved upon by designs found using new, autonomously generated rules!
Experiment Setup:
Ran a genetic algorithm 5 times with a solution length of 150, population size of 1000 and 100 generations using the new rules
Same population size and generations used to find the expert rule solutions

## Slide 21: Research Questions
Will starting the search from a small, feasible model decrease the time needed to find a solution?
Can autonomously generated rules outperform those created by domain experts?
Can other algorithms search the model-space better than a genetic algorithm?

## Slide 22: New Algorithm: Genetic Algorithm Problems
The Crossover Operation
Add Battery
Add Solar Panel
Add Chem Propulsion
Add Ka-Band Comm
Add Electric Propulsion
Add Spacecraft
Add Payload
Add X-Band Comm
…
…
Problem: Models are
Highly Coupled
Crossover
Two High Performing Solutions

## Slide 23: New Algorithm: Memetic Algorithms Overview
Burke et al. 1996
Starting Point
Solution After Running Genetic Algorithm
Solution After Running Hill Climbing
Hill Climbing
Moving in the Direction of the Gradient

## Slide 24: New Algorithm: Algorithm Comparison
Relevant Pros and Cons
 | Multi-Objective Genetic Algorithms | Multi-Objective Hill Climbing
Pros | Crossovers can make large jumps in model space | Can fine tune solutions because searches for the best “nearby” solutions
Cons | Can make jumps too large in the search space to converge to optima | Can get stuck in plateaus and in local minima/maxima because only searches “nearby”
Genetic Algorithms and Hill Climbing Have Opposite Strengths and Weaknesses

## Slide 25: New Algorithm: Implementation
Extended Framework to Allow for Multi-Objective Local Search Algorithms and Implemented MO Hill Climbing
NEW
Extended Framework to Allow Users to Combine Existing Algorithms
NEW
Multi-Objective Hill Climbing in Search-Based Model Design
Only previous work in the field* linearized objectives into one function and used single objective hill climbing
Multi-Objective Memetic (Hybrid) Algorithms in Search-Based Model Design
To my knowledge no work has been published on memetic algorithms
* A Local and Global Tour on MOMoT, Bill et al. 2017

## Slide 26: New Algorithm: Approach
Proposed Memetic Algorithm
Genetic
Algorithm
Multi-Objective
Hill Climbing
Genetic
Algorithm
Multi-Objective
Hill Climbing
Exploration
Exploitation
Exploration
Exploitation

## Slide 27: New Algorithm: Results
New Memetic Algorithm: Application to Cave Exploration Mission
On Average 751 More Fesaible Designs Examined with the memetic algorithm!

## Slide 28: New Algorithm: Results
Proposed Memetic Algorithm: Application to Interferometry Mission
Genetic
Algorithm
Multi-Objective
Hill Climbing
Genetic
Algorithm
Multi-Objective
Hill Climbing

## Slide 29: New Algorithm: Results
Of the Designs Found Using a Genetic Algorithm, 83% were Improved Upon by Designs Found Using a Memetic Algorithm!
Genetic Algorithm vs Memetic Algorithm on the Interferometry Mission
Experiment Setup:
Ran a genetic algorithm (NSGA-II) and a Memetic Algorithm 5 times with a solution length of 150, population size of 1000 and 100 generations using the new rules then the solutions were compared

## Slide 30: New Algorithm: Results
Of the Designs Found Using Expert Crafted Rules and a Genetic Algorithm, 79% were Improved Upon by Designs Found Using the New Rules and a Memetic Algorithm!
Expert Crafted Rules + Genetic Algorithm
vs Autonomously Generated Rules + Memetic Algorithm
Experiment Setup:
Ran a genetic algorithm 5 times with a solution length of 150, population size of 1000 and 100 generations using the new rules
Same population size and generations used to find the expert rule solutions

## Slide 31: Conclusions
Will starting the search from a small, feasible model decrease the time needed to find a solution?
  Yes, was able to find a feasible solution to the Mars Cave Exploration Case Study in on average 5,770 fewer iterations!
  Caveat: may be more sensitive to restarts
Can autonomously generated rules outperform those created by domain experts?
  Yes, with all else equal, 63% of the solutions found by expert crafted rules were Pareto dominated!
Can other algorithms search the model-space better than a genetic algorithm?
  Yes, using a memetic algorithm 79% of the solutions found using a genetic algorithm and hand crafted rules were Pareto dominated and 83% of the solutions found using a genetic algorithm and the new rules. On average increased the number of feasible solutions evaluated on the Mars Cave Exploration Mission all else equal by over 1000%!

## Slide 32: Future Work and Limitations
Limitations
It has been shown that autonomously generating a starting location and exploration rules can outperform those those created by a user. However, the results from the solver are only as good as the model that is input.
Future Work
Check if a user input design problem can have a feasible solution
  Thought: convert the model representation to a boolean formula and use a satisfiability solver, such as Z3 (see: Sandeep Neema et al.)
Currently, exploration rules are chosen from the set of rules uniformly. Choosing rules according to other probability solutions should be explored
  Thought: choose exploration rules according to a probability based on the height of the model element being added in the composition hierarchy

## Slide 33: Thank You!
Special thanks to Dr. Sebastian Herzig for his help and guidance this summer and JPL’s Education Office for hosting me! I have had an amazing summer!

## Slide 34: Acknowledgments
This research was carried out in part at the Jet Propulsion Laboratory, California Institute of Technology, under a contract with the National Aeronautics and Space Administration.

## Slide 36
Backup Slides

## Slide 37: Motivation
Multi-Spacecraft Mission Design: The Case for Computational Methods
Antennas: 6
Solar Panels: 6
CPUs: 2
Cameras: 3
Buses: 7
Propulsion: 3
Attitude Actuators: 10
Launch Adapters: 7
Possible CubeSats:
211,680
Choosing
1 from each
Category
Possible Missions:
Choosing only 2 CubeSats
Notes: 5

## Slide 38: Motivation
Multi-Spacecraft Mission Design
Credit: ESA
Credit: NASA
Fault Tolerance
Science Needs
Notes: 5

## Slide 39: New Algorithm: Why Use a Memetic Algorithm?
Fighting Conventional Wisdom
Claim:
Genetic Algorithms are not well suited to searching model space
Justification:
Crossovers can make big are likely not valid models
Success of a solution can not be attributed to the success of the substrings (for this same reason hill climbing algorithms generally outperform genetic algorithms on the Traveling Salesman Problem without specially tailored mutation and crossover operations)
Proposed Solution:
Once a feasible solution is found, search around the solution by making small changes (additions or subtractions) to the model
Conventional Wisdom
Genetic Algorithms perform better than Hill Climbing because the crossover operation helps get out of local minima
Genetic Algorithms can get stuck in local minima if the maintained population lacks diversity
Some algorithms maintain diversity by favoring solutions with diverse objective values
Work done by a previous intern showed that models with similar objective values can be very different